KPC-ZA880NH 880x Power Zoom Color CCD Camera High Resolution Sony ¼” Super HAD CCD 480 TV Line Built-In 22x Optical Power Zoom Lens 40x Digital Zoom On-Screen-Display Setting Auto Fucus/Exposure

Image Sensor Interline 1/4” Sony Super HAD CCD Total Pixels 811H x 508V Effective Pixels 768H x 494V Horizontal Resolution More than 480 TV Lines Lens 22x Zoom Lens (f=3.9~85.8mm) F1.6(Wide)~F3.7(Tele) Minimum Shooting Distance 0.01m(Wide) / 1m(Tele) Zoom 22x Optical, 40x Digital Scanning Frequency 15.734(H), 59.944(V)KHz Scanning System 2:1 Interlace Min. Illumination 1.0 Lux / 30 IRE Electronic Shutter 1/60~1/10,000 Sec. Video Focus Auto/Manual (Near-Far) OSD On/Off (Function OSD, Sub-Key OSD, Menu OSD) Camera Control RS-232C, RS-485, Controller, A/D Key Position Preset 64 Camera ID On/Off S/N Ratio More than 48dB Video Output 1.0 Vp-p, Composite 75 Ohm Protocol Default / Pelco-D Sync. System Internal Dimensions 2.6W x 2.6H x 4.4L Inch Operating Temperature -10°C to 50°C Storage Temperature -20°C to 60°C Weight 0.8 lbs (approx) Power Consumption 230mA Power Supply DC 12V ±10% / Max 4.2W / 350mA *Above specification and design subject to change without notification