MTR/LCD19 19” LCD MONITOR

Size 19 inch Type A-Si TFT Active Matrix Viewing Angle (H/V) 150/130(CR≥10) Pixel Pitch (H/V) 0.294 mm (H x V) Resolution 1280 x 1024 Contrast Ratio 500 : 1 Luminance 280 cd/㎡ Active Display Size (H x V) 376.32 x 301.056 mm Display Color 16.2 Mil Video R.G.B Analog Sync H/V - Separate Connector 15 pin D-sub Horizontal 30kHz ~ 80 kHz Vertical 60~75Hz Max. Resolution (Analog) 1280 x 1024 @ 75Hz Analog 720 x 400 @ 70 Hz, 640 x 480 @ 60/72/75 Hz, 800x600 @ 56/60/72/75 Hz, 1024 x 768 @ 60/70/75 Hz, 1280 x 1024 @ 60/75 Hz VESA Arm 7.5 x 7.5 ㎝ Audio system 2W x 2ch / Earphone Jack Stand Tilt Stand VESA Arm 7.5 x 7.5 ㎝ User Control Brightness, Contrast, H/V-Position, Auto, phase, Color temperature selection, OSD location adjustment, Language, Reset, Exit Power Source 100 ~ 240V AC 1.0A Power Consumption 60W (Max.) Safety & Regulations FCC, CE, CB, VCCI, UL/CUL, CCC, PSE, GOST,TUV-GS, C-Tick, NOM, BSMI, EK, MIC Unit Dimensions & Weight 16.9 x 17 x 7.8 inch, 10.8 lbs *Above specifications and design subject to change without notification

# Text boxes

- 19 Inch Viewable SXGA(1280x1024) LCD

- Brightness 280 cd/㎡

- Contrast Ratio 500 : 1 (Typical)

- Response Time 8ms

- Analog Interface

- Built-in power supply

- Power Management (VESA DPMS)

- Plug-and-Play (VESA DDC2B Compatibility)

- TCO'03 Certified

- Support VESA Physical Mounting Interface