NVC-IR045VA COLOR IR CAMERA with Varifocal Lens

TV System NTSC Scanning System 525 lines 2:1 interlace Scanning Frequency H: 15.734Hz / V: 59.94Hz Total Pixels 811(H) x 508(V) Effective Pixels 768(H) x 494(V), 380K Horizontal Resolution 420(H) TV lines Pick-Up Device 1/3” Sony Super HAD CCD Electronic Shutter 1/60 ~ 100,000 Minimum Illumination 0.1 Lux (0.00 Lux with CDs sensor on) S/N Ratio More than 45dB White Balance Automatic Gamma Correction 0.45 Video Out VBS 1.0Vp-p composite 75 ohm Sync System Internal Lens DC Auto Iris Varifocal Lens (4mm~9mm) Power Supply DC 12V Dimensions 3.2 (diameter) x 6 (L) inch Weight 3.5 lbs * above specifications and design subject to change without notice

# Text boxes

- 1/3” Sony Super HAD CCD

- 420 TV Line

- 4~9mm Varifocal Auto Iris Lens

- 0.1 Lux (0.00 Lux with CDs Sensor On)

- 12V DC

- 45 LEDs