NVC-IR050 IR Camera with 50 LEDs

Image Sensor 1/3” Sony Super HAD CCD CCD Total Pixel 510H x 492V Scanning System 2:1 Interlaced Sync. System Internal Resolution 420 TV lines Min. Illumination 0.1 Lux (CDS on 0.00 Lux) S/N Ratio More than 50dB Gamma Characteristic r=0.45 Video Output 1.0Vp-p 75 ohm Electronic Shutter 1/60~1/100,000 Power Supply DC 12V 1000mA Power Consumption 520mA Type Lens 6mm fixed lens F:1.8 Operating Temperature -10°C ~ 50°C Dimensions 2.8Ø x 3.9L inch (approx.) Weight 2 lbs (approx.) *Above specifications and design subject to change without notification.

# Text boxes

- 1/3” Sony Super HAD CCD

- 0.1 Lux (CDs on: 0.00 Lux)

- 6mm fixed lens

- Built-In 50 IR LED

- 420 TV Lines