SK-2005 B&W MINI SQUARE CAMERA

Image Sensor 1/3” B&W CCD Effective Pixels 510(H) x 492(V) H. Resolution 400 TV line Min. Illumination 0.5 Lux Audio Gain 40dB±2dB Audio Max Output 600 Ohm Max. 3Vp-p Frequency Response 300Hz~20,000Hz Audio S/N Ratio -45dB±10% Synchronizing System Internal Scanning System 2:1 interlace Video Output 1.0Vp-p (sync. Negative) termination 75Ω S/N Ratio More than 45dB or more (AGC off) Gain Control Automatic Electronic Shutter 1/60~100,000 sec Gamma Correction r=0.45 Lens 4.3mm fixed lens, f/2.0 Power Source DC 12V Power Consumption Max 110mA Reverse Polarity Protection Yes Humidity RH 95% Max Preservation Temperature -40°C~60°C RH 95% Max Operation Temperature -10°C~50°C Dimensions 1.2 x 1.2 inch Case Material Aluminum *Above specifications and design subject to change without notification

# Text boxes

- 1/3” Sony CCD

- Compact Size (1.2” x 1.2”)

- Video, audio, and power cable included

- 3.7mm Lens

- 12V DC

- Audio Output

- Built-In Microphone